INSTALLATION INSTRUCTIONS FOR HOT FIX 12GRIDSMC02 ON HPUX 64BIT

BEFORE DOWNLOADING:

The hot fix 12GRIDSMC02 addresses the issue(s) in 1.2 of SAS Grid Manager Plug-ins for SAS Management Console software on HPUX 64BIT as documented in the "Issue(s) Addressed" section of the hot fix download page:

http://ftp.sas.com/techsup/download/hotfix/gridsmc12.html#12gridsmc02

IMPORTANT NOTE(S):

1.  You must have SAS Grid Manager Plug-ins for SAS Management Console 1.2 installed on your

system before applying this hot fix.

2.  The hotfix must be installed using the same userid that performed the initial SAS Grid

Manager Plug-ins for SAS Management Console 1.2 installation.

3.  You must have Administrator Privileges on your CLIENT or SERVER machine.

4.  All currently active SAS sessions, daemons, spawners and servers must be terminated before

applying this hot fix.

INSTALLING THIS HOT FIX:

1.  Technical Support strongly suggests that you back up the files being replaced by this hot fix. You should always try to include the current date in the name of the backup file created to distinguish between versions of backup files.  By doing this you will maintain a history of the file, which will be helpful when multiple iterations of a hot fix have been applied to the same file.

For example,

cp  sas.foo.jar  sas.foo.jar.02132008

where 02132008 is the date when the hot fix is applied.

The .<date> extension MUST be appended AFTER the .jar extension as it appears above.

The files that should be backed up for this hot fix are listed in Step #5 below.

2.  Extract the contents of 12gridsmc02h6.tar into a temporary directory, for  example /tmp/12gridsmc02h6.

$> mkdir /tmp/12gridsmc02h6

$> cd /tmp/12gridsmc02h6

$> tar -xf $HOME/12gridsmc02h6.tar

where $HOME is the location to where the tar file was downloaded.

The tar command will extract the following files to the temporary directory:

h64/Setup_HPUX_11x

h64/media.inf

h64/setup.jar

3.  Verify that Setup_Solaris_Sparc has execute permission.  If it does not, use the 'chmod' command to make it executable:

$> cd /tmp/12gridsmc02h6/h64

$> chmod 755 Setup_HPUX_11x

4.  Initiate the installation wizard

$>  export DISPLAY=<nodename>:0           <==== set your display

$>  cd /tmp/12gridsmc02h6/h64

$>  ./Setup_HPUX_11x

This will initiate the Java install wizard.  Follow the prompts to complete the installation.

5.  To verify the installation of the hot fix confirm that the file(s) in the location(s) below have been updated to the level indicated by the date provided:

<!SASHOME>/SASManagementConsole/9.1/plugins/com_platform_drm.jar

Date: 10/26/07 (EST)

<!SASHOME>/SASManagementConsole/9.1/plugins/com_platform_drm_ac.jar

Date: 10/26/07 (EST)

<!SASHOME>/SASManagementConsole/9.1/plugins/com_platform_drm_em.jar

Date: 10/26/07 (EST)

<!SASHOME>/SASManagementConsole/9.1/plugins/com_platform_drm_loginmodules.jar

Date: 10/26/07 (EST)

<!SASHOME>/SASManagementConsole/9.1/plugins/com_platform_drm_rm.jar

Date: 10/26/07 (EST)

<!SASHOME>/SASManagementConsole/9.1/plugins/com_platform_drm_util.jar

Date: 10/26/07 (EST)

<!SASHOME>/SASManagementConsole/9.1/plugins/com_platform_drm_wm.jar

Date: 10/26/07 (EST)

<!SASHOME>/SASManagementConsole/9.1/plugins/sas.smc.gridmanager.platform.jar

Date: 03/01/07 (EST)

This completes the installation of hotfix 12GRIDSMC02 on HPUX 64BIT .